## Slide 1
Photo from Elm Creek Restoration Project
Lenhart, Brooks, and Magner
Water storage in the Minnesota River
Dr. Karen Gran
Earth & Environmental Sciences
University of Minnesota Duluth
December 2019

## Slide 2: How is hydrology changing in MN River?
Annual flow metrics normalized by the 1950–2010 mean. Data from 12 gages on Minnesota River.
Kelly et al., 2017

## Slide 3: How is hydrology changing in Red River?
Kelly et al., 2017

## Slide 4: Why is hydrology changing?
Drainage and Climate
Schottler et al., 2013
1940
2012
Kelly et al., 2017

## Slide 5: Why are higher flows a problem?
Flooding
Erosion
  Infrastructure damage
  Sediment loading
Photo by SWNews.com

## Slide 6: What is the value of water storage?
REDUCE Flooding
REDUCE Erosion
  Infrastructure damage
  Sediment loading
REDUCE Nutrient export
Photo by SWNews.com

## Slide 7
Photo: Star Tribune
Minnesota
Mississippi
MN River is sensitive to increases in flow.
There is a tight connection between hydrology and erosion that is related to the geomorphic history of the watershed.

## Slide 8
J. Czuba

## Slide 9
Above the knickpoint
Photos by Carrie Jennings

## Slide 10
Photos by Carrie Jennings
Below the
knickpoint

## Slide 11
Above
knickpoint
Below
Knickpoint
Bluffs
Ravines
Streambanks
Uplands
Where is sediment coming from?
Uplands
Ravines
Streambanks
Bluffs
Floodplains
Lakes
Notes: add land use- general and hi-res yields
surficial geology, soils maps
sediment loads

## Slide 12: Sediment sources in Greater Blue Earth River Basin are predominantly related to near-channel erosion
Upland
Ravine
Bluff
Streambanks
Le Sueur
Watonwan
Blue Earth
Total (GBERB)

## Slide 13
The amount of sediment has increased over time
Year
0
200
400
600
800
Sedimentation Rate (103 Mg y-1)
1500
1600
1700
1800
1900
2000
Minnesota River
Mississippi +
St. Croix Rivers
From Engstrom et al., 2009
Kelley & Nater,2000
Lake Pepin Record

## Slide 14
Belmont et al. (2011)
Pre-Euro settlement conditions; Most sediment derived from non-field sources
Rise of agriculture; Increase in sedimentation; Shift in sources to predominantly field sediment
Sediment loads stay high; Shift in sources back to non-field
% Field
High
Low
Sedimentation record with sediment fingerprinting data

## Slide 15
Geomorphic Response to changing flows
Rivers are getting wider over time
Figure from Wes Lauer

## Slide 16
At what flows is erosion happening?
Cho et al., 2019
Near-channel erosion rates increase at high flows.
If we can decrease flows, we can lower erosion rates along bluffs.
Sediment Supply from
Incised Zone (Mg/day/km)
Normalized River Discharge (m3/s/km2)

## Slide 17
At what flows is erosion happening?
Cho et al., 2019
Near-channel erosion rates increase at high flows.
If we can decrease flows, we can lower erosion rates along bluffs.
Sediment Supply from
Incised Zone (Mg/day/km)
Normalized River Discharge (m3/s/km2)

## Slide 18
How can we reduce sediment loading?
Photo: Star Tribune
NRCS
MN DNR
NRCS
Photo: StCroix360; Washington Conservation District
Lesueurriver.org
Rice SWCD
?

## Slide 19: CSSR Collaborative for Sediment Source Reduction
Goal: To identify a consensus strategy for reducing sediment loading in the Greater Blue Earth watershed using a decision framework that incorporates the best available scientific information, accounts for uncertainty, and provides a model for decision making throughout the Minnesota River Basin.

## Slide 20
Stakeholder Group
2012
2013
2014
2015
1
2
3
4
5
6
7
2016
2017
8
9

## Slide 21
Route water and sediment downstream
Apply mgmt options on landscape
Determine costs
Determine sediment loads
User specifies management options:
Type, Extents, Rates, Costs
Collaborative for Sediment Source Reduction
Greater Blue Earth River
Management Option Simulation Model

## Slide 22
How do we get the most ‘bang for the buck’?
Cho et al., 2019
Annual Cost [$/yr]
Annual Sediment Load Reduction [%]
Green = buffers, grassed waterways
Blue = water storage
Orange = water storage + bluff stabilization
Costs
Sediment load reduction
Notes: Scenario 1 includes 12,000 acres of water storage (about 20% of available candidate sites) and 24,000 m of bluff stabilization (about 30% of available candidate sites) and provides an annual sediment load reduction of 79,000 Mg (43% reduction) at an annual cost of $21 million. Scenario 2 increases acreage in water conservation to about 25% of available sites and river length in bluff stabilization to about 40% of available sites and incorporates cover crops to 30% of total agricultural land. This scenario produces an annual reduction in sediment loading of 95,000 Mg (51% reduction) at an annual cost of $35 million.

## Slide 23
Consensus!
https://conservancy.umn.edu/handle/11299/191082

## Slide 24: Summary of findings
1. Ravines that are large local sources of sediment can be targeted. Investment in stabilizing these ravines is worthwhile, but not sufficient to reduce sediment loading to meet water quality standards.

## Slide 25: Summary of findings
2. Eroding bluffs that threaten infrastructure and produce exceptionally large amounts of sediment can be targeted. Investment in stabilizing these bluffs is worthwhile, but bluff stabilization is not the most effective solution for long-term reduction in sediment loading across the watershed.

## Slide 26: Summary of findings
3. Achieving water quality standards will require priority investment in more temporary water storage to reduce high river flows and bluff erosion. This is a critical component of a strategy to reduce sediment in the Minnesota River.

## Slide 27
U of M Southwest Research and Outreach Center
Elm Creek Restoration Project, Lenhart, Brooks & Magner
BE County Ditch 57 Restoration Project, ISG
Swift County JD 8 Restoration Project, Kriter, Magner and others

## Slide 28
Wetlands also decrease nitrogen concentrations
Hansen et al., 2018
Nature Geoscience
Notes: Le Sueur, Cottonwood, and Chippewa

## Slide 29
Field management | 
 | Cover crops
 | Grassed waterway
 | Fertilizer management
 | Isolated marsh
 | Isolated pond
Near channel management | 
 | Buffer strip
 | Reservoir
 | Fluvial marsh
 | Ravine tip stabilization
 | Bluff stabilization

## Slide 30: Where do you install water storage?
MOSM explored large-scale placement Greater Blue Earth basin
SWAT model explored large-scale placement Le Sueur basin
Multi-model: sediment, nitrate in Le Sueur basin
PTMApp (Prioritize, Target, and Measure)
ACPF (Agricultural Conservation Planning Framework)
Restorable Wetland Prioritization Tool (MN DNR/NRRI)
Anywhere you can

## Slide 31
Funding provided by:
Nate Mitchell, UMD
Todd Campbell, ISU
Peter Hawthorne, UM
Cathy Kling, Cornell
Sergey Rabotyagov, UW
Collaborators:
Patrick Belmont, USU
Peter Wilcock, USU
Ben Hobbs, JHU
Carrie Jennings
Stephanie Day, NDSU
Wes Lauer, Seattle U
Barbara Heitkamp, UM
Jeff Marr, UM
Efi Foufoula-Georgiou, UI
Jacques Finlay, UM
Brent Dalzell, UM
Chris Lenhart, UM
CSSR
Collaborative for
Sediment Source Reduction
Acknowledgements
None of our work would be possible without the tireless and meticulous work of innumerable state and local agency staff and the interest and support of south central Minnesotans.
Anna Baker, UM
Amy Hansen, UM
Sara Kelly, USU
Karthik Kumarasamy, USU
Martin Bevis , UMD
Se Jong Cho, JHU/UM
Jon Czuba, UM
Christy Dolph, UM